## Slide 1
TEAM 3091 · REBUILT
FRC 2026
Robot Code
A student-focused walkthrough of the command-based architecture
powering Team 3091's 2026 competition robot.
WPILib 2026 · Java 17 · REVLib · PhotonVision · Command-Based Framework

## Slide 2
WHAT WE'LL COVER
Table of Contents
01
What is FRC & Command-Based Programming?
02
Project Structure & File Overview
03
The Robot Lifecycle — TimedRobot Modes
04
RobotContainer — The Command Dispatcher
05
Constants.java — Centralized Configuration
06
Subsystems — Drive, Collector, Loader, Shooter, CollectorArm
07
Vision Subsystem & Distance Estimation
08
Commands — How Robots Respond to Input
09
Autonomous Routines
10
Controller Bindings & Hardware Map

## Slide 3
01 — INTRODUCTION
What is FRC & Command-Based Programming?
FIRST Robotics Competition
FRC is a high-school robotics competition where students build full-size robots to compete on a game field each January–April. Robots are programmed in Java, C++, or Python using the WPILib framework provided by Worcester Polytechnic Institute. The robot runs on a roboRIO — a real-time Linux controller that runs your Java code at 50 Hz (every 20ms).
Command-Based Framework
WPILib's command-based architecture separates robot code into two key concepts: Subsystems — Hardware components (motors, sensors). One class per mechanism. Only one command can use a subsystem at a time. Commands — Actions that use subsystems. They have initialize(), execute(), end(), and isFinished().
The
CommandScheduler manages everything automatically every 20ms loop.

## Slide 4
02 — PROJECT STRUCTURE
Project Structure
src/main/java/frc/robot/
├── Main.java ← Entry point
├── Robot.java ← TimedRobot lifecycle
├── RobotContainer.java ← Wires everything together
├── Constants.java ← All hardware config values
├── commands/
│ ├── TeleopDrive.java
│ ├── RunCollector.java
│ ├── RunCollectorArm.java
│ ├── RunLoader.java
│ ├── RunShooter.java
│ └── Autos.java ← Auto routines
└── subsystems/
├── Drive.java
├── Collector.java
├── CollectorArm.java
├── Loader.java
├── Shooter.java
└── Vision.java
Main.java is a single line — just starts the robot.
Robot.java is the heartbeat. It calls the CommandScheduler every 20ms.
RobotContainer wires subsystems + commands + controller bindings.
Constants.java holds all motor ports, speeds, and tuning values in one place.

## Slide 5
03 — ROBOT LIFECYCLE
The Robot Lifecycle — TimedRobot Modes
DISABLED
Robot on but not moving.
disabledInit() → disabledPeriodic()
Commands still scheduled but motors held at 0.
AUTONOMOUS
Pre-programmed 15-second period.
autonomousInit() schedules the auto command.
autonomousPeriodic() runs every 20ms.
TELEOP
Driver-controlled period.
teleopInit() cancels the auto command.
Controller bindings take over.
TEST
Development mode.
testInit() cancels ALL running commands.
Useful for testing individual mechanisms.
CommandScheduler.getInstance().run()
Called every 20ms in robotPeriodic(). Polls button triggers, runs active commands, checks subsystem default commands, and calls all subsystem periodic() methods. This single line IS the entire robot's brain loop.

## Slide 6
03 — ROBOT LIFECYCLE
Main.java & Robot.java
Main.java
public static void main(String... args) {
RobotBase.startRobot(Robot::new);
// That's it! WPILib handles the rest.
}
Main.java is intentionally minimal. WPILib's RobotBase takes a factory method and manages the main loop internally.
Robot.java — key sections
public Robot() {
m_robotContainer = new RobotContainer();
CameraServer.startAutomaticCapture();
}
public void robotPeriodic() {
CommandScheduler.getInstance().run();
}
public void autonomousInit() {
m_autonomousCommand =
m_robotContainer.getAutonomousCommand();
if (m_autonomousCommand != null)
CommandScheduler.getInstance()
.schedule(m_autonomousCommand);
}
public void teleopInit() {
if (m_autonomousCommand != null)
m_autonomousCommand.cancel();
}
► Key Insight
Robot.java's constructor creates RobotContainer once, and also starts the camera stream. Every other line is just calling into the CommandScheduler or managing the auto command lifecycle.

## Slide 7
04 — ROBOTCONTAINER
RobotContainer.java — The Glue
SUBSYSTEMS
Drive.java
Collector.java
CollectorArm.java
Loader.java
Shooter.java
Vision.java
RobotContainer
1. Instantiate all
subsystems
2. Create both
PS4 controllers
3. Set default
command for Drive
4. configureBindings()
— map buttons→commands
5. getAutonomousCommand()
— returns auto
COMMANDS
TeleopDrive.java
RunCollector.java
RunCollectorArm.java
RunLoader.java
RunShooter.java
Autos.java
NOTE: Think of RobotContainer as the main() of robot logic — it doesn't DO anything directly; it just wires things together.

## Slide 8
05 — CONSTANTS
Constants.java — Centralized Configuration
public final class Constants {
public static class DriveConstants {
public static final int kLeftFrontMotorPort = 0; // PWM ports 0-3
public static final int kRightFrontMotorPort = 2;
public static final boolean kLeftMotorsInverted = true;
public static final double kJoystickDeadband = 0.01;
public static final double kMaxSpeed = 1.0;
public static final double kTriggerScale = 0.8; // Triggers run at 80% max
}
public static class ShooterConstants {
public static final int kShooterMotorPort = 5; // PWM port 5
public static final double kShooterPresetMin = 0.1; // X button — 10%
public static final double kShooterPresetLow = 0.4; // D-pad ← — 40%
public static final double kShooterPresetHigh = 0.7; // D-pad → — 70%
}
public static class CollectorArmConstants {
public static final double kCollectorArmRetractSpeed = 0.5;
public static final double kCollectorArmExtendSpeed = -0.3; // negative = extend
public static final double kCollectorArmExtendRampRate = 0.015; // per 20ms cycle
public static final double kCollectorArmHoldSpeed = 0.05; // prevents slack
}
}
No magic numbers
Every motor port and speed has a name. Reading the code tells you what's happening.
Single source of truth
Change a port number in one place — all code that uses it updates automatically.
Easy tuning
Drivers can adjust kMaxSpeed or kJoystickDeadband without touching command logic.
Static inner classes
Groups related constants. DriveConstants only holds drive values.

## Slide 9
06 — SUBSYSTEMS
Subsystems — Hardware Abstraction Layer
Each subsystem wraps one piece of hardware. Commands call subsystem methods — they never touch motors directly.
Drive
PWM 0-3 · Spark (PWM)
4-motor tank drive. Left and right MotorControllerGroups. tankDrive(left, right) method.
Collector
CAN ID 3 · REV SPARK MAX
Intake motor. run(speed), stop(). Only mechanism using CAN bus (brushless motor).
CollectorArm
PWM 6 · Spark (PWM)
Winds/unwinds a string to raise/lower collector. retract(), extend(), setSpeed(), stop().
Loader
PWM 4 · Spark (PWM)
Feeds game pieces into the shooter. run(), run(speed), stop().
Shooter
PWM 5 · Spark (PWM)
Launches game pieces. run(speed), stop(). Used with preset speeds from Constants.
Vision
USB / Network · PhotonVision
Detects targets, estimates distance, calculates required shooter speed via linear interpolation.

## Slide 10
06 — DRIVE SUBSYSTEM
Drive.java — 4-Motor Tank Drive
public class Drive extends SubsystemBase {
private final Spark m_leftFront, m_leftBack; // PWM 0, 1
private final Spark m_rightFront, m_rightBack; // PWM 2, 3
private final MotorControllerGroup m_leftMotors;
private final MotorControllerGroup m_rightMotors;
public Drive() {
m_leftMotors = new MotorControllerGroup(m_leftFront, m_leftBack);
m_rightMotors = new MotorControllerGroup(m_rightFront, m_rightBack);
m_leftMotors.setInverted(DriveConstants.kLeftMotorsInverted); // true
m_rightMotors.setInverted(false);
}
public void tankDrive(double leftSpeed, double rightSpeed) {
// Clamp to [-1.0, 1.0] and scale by kMaxSpeed
leftSpeed = Math.max(-1.0, Math.min(1.0, leftSpeed)) * kMaxSpeed;
rightSpeed = Math.max(-1.0, Math.min(1.0, rightSpeed)) * kMaxSpeed;
m_leftMotors.set(leftSpeed);
m_rightMotors.set(rightSpeed);
}
@Override
public void periodic() {
SmartDashboard.putNumber("Drive/Left Speed", m_leftFront.get());
SmartDashboard.putNumber("Drive/Right Speed", m_rightFront.get());
}
}
▶ SubsystemBase
Extends WPILib's base class. This registers the subsystem with the CommandScheduler and enables the periodic() callback.
▶ MotorControllerGroup
Groups two motors to run in sync. Setting one speed controls both left (or right) motors simultaneously.
▶ setInverted(true)
Left motors are inverted because they physically face the opposite direction on the robot chassis.
▶ periodic()
Called every 20ms automatically. Ideal for logging sensor data to SmartDashboard for debugging.

## Slide 11
06 — SUBSYSTEMS
Collector & Loader Subsystems
Collector.java
public class Collector extends SubsystemBase {
private final SparkMax m_motor; // CAN ID 3
public Collector() {
m_motor = new SparkMax(
CollectorConstants.kCollectorCanId,
MotorType.kBrushless);
}
public void run(double speed) {
m_motor.set(speed);
}
public void stop() { m_motor.set(0.0); }
}
Uses REV SPARK MAX over CAN bus (not PWM). This brushless motor controller provides higher precision. The CAN protocol lets you daisy-chain many devices on two wires.
Operator L2 (analog trigger) controls speed proportionally. L1 runs in reverse to eject jammed pieces.
Loader.java
public class Loader extends SubsystemBase {
private final Spark m_motor; // PWM 4
public Loader() {
m_motor = new Spark(
LoaderConstants.kLoaderMotorPort);
m_motor.setInverted(
LoaderConstants.kLoaderInverted);
}
public void run() {
m_motor.set(LoaderConstants.kLoaderSpeed);
}
public void stop() { m_motor.set(0.0); }
}
Simple PWM Spark motor controller. The loader feeds game pieces from storage into the shooter mechanism.
Operator Circle holds to feed. Operator Square reverses to unjam. Fixed speed defined in LoaderConstants.kLoaderSpeed = 1.0 (full power).

## Slide 12
06 — COLLECTORARM
CollectorArm — Soft-Start Ramp Logic
// RunCollectorArm.java — the command that controls the arm
public enum CollectorArmMode { RETRACT, STOP, EXTEND }
@Override
public void execute() {
switch (m_modeSupplier.get()) {
case RETRACT -> {
m_rampedExtendSpeed = 0.0; // Reset ramp
m_arm.retract(); // Full speed wind-up: +0.5
}
case EXTEND -> {
// Gradually ramp toward target extend speed each 20ms loop
// Prevents a jerk from suddenly applying -0.3 (gravity assist)
double target = CollectorArmConstants.kCollectorArmExtendSpeed; // -0.3
m_rampedExtendSpeed = Math.max(
m_rampedExtendSpeed - kCollectorArmExtendRampRate, // subtract 0.015/cycle
target // clamp at -0.3
);
m_arm.setSpeed(m_rampedExtendSpeed);
}
default -> {
m_arm.setSpeed(kCollectorArmHoldSpeed); // +0.05 — prevents string slack
}
}
}
Why ramp?
Suddenly applying -0.3 power causes a jerk. Ramping from 0 to -0.3 over 20 cycles (~0.4 seconds) gives a smooth, controlled descent.
Hold speed
When no button is held, +0.05 keeps slight tension on the string. Without this, gravity unwinds the arm slowly.
Enum mode
An enum cleanly models the 3 states (RETRACT / STOP / EXTEND). The Supplier<> allows the command to receive the mode dynamically from a button.

## Slide 13
06 — SHOOTER
Shooter Subsystem & Speed Presets
Shooter.java
public class Shooter extends SubsystemBase {
private final Spark m_motor; // PWM 5
public void run(double speed) {
m_motor.set(speed); // -1.0 to 1.0
}
public void stop() {
m_motor.set(0.0);
}
}
Speed Presets (from Constants.java)
Button | Constant | Value | Power | Use Case
X button | kShooterPresetMin | 0.1 | 10% | Close range
D-pad ← | kShooterPresetLow | 0.4 | 40% | Medium range
D-pad → | kShooterPresetHigh | 0.7 | 70% | Long range
R2 (analog) | trigger * 1.0 | 0-1.0 | 0-100% | Variable speed
RunShooter.java (command)
public class RunShooter extends Command {
private final Shooter m_shooter;
private final DoubleSupplier m_speed;
@Override
public void execute() {
// Normalize R2: [-1.0, 1.0] → [0.0, 1.0]
double speed = (m_speed.getAsDouble()+1.0)/2.0;
m_shooter.run(speed);
}
@Override
public void end(boolean interrupted) {
m_shooter.stop();
}
@Override
public boolean isFinished() { return false; }
}
The PS4 R2 axis reports [-1.0, 1.0] where -1.0 = fully released and +1.0 = fully pressed. The command normalizes this to [0.0, 1.0] before passing it to the shooter.
isFinished() returns false — this command runs forever until interrupted (button released). This is the pattern for hold-to-run commands.
addRequirements(shooter) tells the scheduler: this command owns the shooter subsystem — no other command can run the shooter while this one is active.

## Slide 14
07 — VISION
Vision.java — PhotonVision Distance Estimation
// Camera constants (measure on your actual robot)
private static final double CAMERA_HEIGHT_METERS = 0.4318; // 17 inches above floor
private static final double TARGET_HEIGHT_METERS = 1.8161; // Hub center height
private static final double CAMERA_PITCH_DEGREES = 0.0; // Camera is level
public double getDistanceMeters() {
PhotonTrackedTarget target = result.getBestTarget();
double targetPitchRadians = Math.toRadians(target.getPitch());
double cameraPitchRadians = Math.toRadians(CAMERA_PITCH_DEGREES);
double heightDelta = TARGET_HEIGHT_METERS - CAMERA_HEIGHT_METERS;
// Trigonometry: tan(angle) = opposite/adjacent
return heightDelta / Math.tan(cameraPitchRadians + targetPitchRadians);
}
public double getCalculatedShooterSpeed() {
double distance = getDistanceMeters();
// Linear interpolation: map distance [1m..4m] → speed [0.5..1.0]
double t = (distance - MIN_DISTANCE_METERS)
/ (MAX_DISTANCE_METERS - MIN_DISTANCE_METERS);
t = Math.max(0.0, Math.min(1.0, t)); // clamp to [0,1]
return SPEED_AT_MIN_DISTANCE + t * (SPEED_AT_MAX_DISTANCE - SPEED_AT_MIN_DISTANCE);
}
PhotonVision
Open-source vision library. Runs on a co-processor (Raspberry Pi / OrangePi). Sends targeting data to the robot via NetworkTables.
Trig formula
distance = heightDelta / tan(cameraPitch + targetPitch). As target pitch increases (target appears higher), distance decreases.
Linear Interp
Maps a distance value linearly to a shooter speed. At 1m → 50% power. At 4m → 100% power. Clamped so it never exceeds bounds.

## Slide 15
08 — COMMANDS
Commands — The 4-Method Contract
Every command in WPILib must implement four methods. Together they form a complete lifecycle.
initialize()
Called ONCE when the command is first scheduled. Use for setup — reset sensors, set initial motor speeds.
execute()
Called EVERY 20ms loop while the command is active. This is where motor control logic lives.
end(boolean)
Called when the command finishes or is interrupted. Always stop motors here. interrupted=true means another command took over.
isFinished()
Return true when the command should stop itself. For hold-to-run commands (like RunShooter), this returns false — the trigger interrupt handles stopping.
NOTE: Always call addRequirements(subsystem) in the constructor! This prevents two commands from fighting over the same motor.

## Slide 16
08 — TELEOPDRIVE
TeleopDrive.java — Blended Tank Drive
@Override
public void execute() {
double leftSpeed = m_leftY.getAsDouble(); // Left joystick Y
double rightSpeed = m_rightY.getAsDouble(); // Right joystick Y
// PS4 triggers report [-1.0, 1.0] — normalize to [0.0, 1.0]
double r2 = (m_r2Trigger.getAsDouble() + 1.0) / 2.0;
double l2 = (m_l2Trigger.getAsDouble() + 1.0) / 2.0;
// Apply deadbands — ignore tiny joystick drift
leftSpeed = applyDeadband(leftSpeed, DriveConstants.kJoystickDeadband);
rightSpeed = applyDeadband(rightSpeed, DriveConstants.kJoystickDeadband);
r2 = applyDeadband(r2, DriveConstants.kTriggerDeadband);
l2 = applyDeadband(l2, DriveConstants.kTriggerDeadband);
// Scale triggers (0.8 max — gentler response)
r2 *= DriveConstants.kTriggerScale;
l2 *= DriveConstants.kTriggerScale;
// Triggers add equal boost/brake to BOTH sides (straight forward/backward)
double boost = r2 - l2;
leftSpeed += boost;
rightSpeed += boost;
// Clamp final values to [-1.0, 1.0]
leftSpeed = Math.max(-1.0, Math.min(1.0, leftSpeed));
rightSpeed = Math.max(-1.0, Math.min(1.0, rightSpeed));
m_drive.tankDrive(leftSpeed, rightSpeed);
}
▶ DoubleSupplier
Instead of passing a value directly, the constructor takes a lambda () -> controller.getLeftY(). The command reads it fresh every 20ms.
▶ Deadband
Controllers have physical drift — the joystick reports small non-zero values even at rest. Deadband ignores anything below 0.01.
▶ Blended control
R2/L2 add a constant boost to both sides. This lets you use joysticks for steering while holding R2 for speed — all blend additively.
▶ Default command
TeleopDrive is set as Drive's default command. It runs automatically whenever no other command requires the Drive subsystem.

## Slide 17
09 — AUTONOMOUS
Autonomous Routines — Autos.java
driveAndShoot() — fallback auto
new SequentialCommandGroup(
// 1. Drive forward 2 seconds
Commands.run(() ->
drive.tankDrive(0.5, 0.5), drive)
.withTimeout(2.0),
// 2. Stop
Commands.runOnce(drive::stop, drive),
// 3. Shoot + load simultaneously
Commands.parallel(
Commands.run(() ->
shooter.run(-kShooterPresetHigh), shooter),
Commands.run(loader::run, loader)
).withTimeout(10.0),
// 4. Stop both
Commands.runOnce(shooter::stop),
Commands.runOnce(loader::stop)
)
Simple timed sequence. No vision needed. Reliable fallback if the camera isn't working. Drive forward → stop → shoot for 10s.
visionDriveAndShoot() — primary auto
new SequentialCommandGroup(
// 1. Drive forward until target seen
// (or max 3 seconds — safety timeout)
Commands.run(() ->
drive.tankDrive(0.4, 0.4), drive)
.until(vision::hasTarget)
.withTimeout(3.0),
// 2. Stop
Commands.runOnce(drive::stop, drive),
// 3. Shoot at vision-calculated speed
Commands.parallel(
Commands.run(() -> {
double spd = vision.getCalculatedShooterSpeed();
shooter.run(spd > 0 ? spd : kShooterPresetHigh);
}, shooter),
Commands.run(loader::run, loader)
).withTimeout(10.0),
)
Vision-guided auto. Drives toward the goal until the camera sees a target, then stops and shoots at the correct speed for the measured distance. Falls back to 70% power if no target found.

## Slide 18
10 — CONTROLLER BINDINGS
Controller Bindings — configureBindings()
Driver Controller — Port 0
Input | Function
Left Joystick Y | Left side motors (tank drive)
Right Joystick Y | Right side motors (tank drive)
R2 (hold) | Both sides forward (boost)
L2 (hold) | Both sides backward (brake)
Operator Controller — Port 1
Input | Function
R2 (analog) | Shooter — variable speed
L2 (analog) | Collector — variable speed
R1 (hold) | Shooter reverse (unjam)
L1 (hold) | Collector reverse (eject)
Circle (hold) | Loader — run
Square (hold) | Loader reverse (unjam)
X button | Shooter 10% preset
D-pad ↑ | Collector arm retract
D-pad ↓ | Collector arm extend
D-pad ← | Shooter 40% preset
D-pad → | Shooter 70% preset
How bindings work in code
// Default command (runs when nothing else uses Drive)
m_drive.setDefaultCommand(new TeleopDrive(
m_drive,
() -> m_driverController.getLeftY(),
() -> m_driverController.getRightY(),
() -> m_driverController.getR2Axis(),
() -> m_driverController.getL2Axis()));
// Trigger: run shooter while R2 is pressed past deadband
new Trigger(() -> m_operatorController.getR2Axis() > -0.95)
.whileTrue(new RunShooter(
m_shooter,
() -> m_operatorController.getR2Axis()));
// Button: run loader while Circle is held
m_operatorController.circle()
.whileTrue(new RunLoader(m_loader));
// Inline command: reverse shooter while R1 held (unjam)
m_operatorController.R1().whileTrue(
m_shooter.runEnd(
() -> m_shooter.run(-kShooterPresetLow),
m_shooter::stop));

## Slide 19
10 — HARDWARE MAP
Hardware Map — Motor Controllers & Ports
PWM Ports (roboRIO)
Port | Motor | Controller | Subsystem
PWM 0 | Left Drive Motor 1 | Spark (PWM) | Drive
PWM 1 | Left Drive Motor 2 | Spark (PWM) | Drive
PWM 2 | Right Drive Motor 1 | Spark (PWM) | Drive
PWM 3 | Right Drive Motor 2 | Spark (PWM) | Drive
PWM 4 | Loader | Spark (PWM) | Loader
PWM 5 | Shooter | Spark (PWM) | Shooter
PWM 6 | Collector Arm | Spark (PWM) | CollectorArm
CAN Bus
CAN ID | Motor | Controller | Subsystem
CAN 3 | Collector Intake | SPARK MAX | Collector.java
SmartDashboard Telemetry
The robot publishes live data to the Driver Station dashboard:
• Drive/Left Speed — current left motor output
• Drive/Right Speed — current right motor output
• Vision/HasTarget — camera sees a target?
• Vision/DistanceMeters — estimated distance
• Vision/ShooterSpeed — calculated shot power
Vendor Libraries (vendordeps/)
REVLib — REV SPARK MAX support
WPILibNewCommands — Command2 framework
PhotonLib — PhotonVision integration
(+ many others for future expansion)

## Slide 20
BUILD & DEPLOY
Getting Code onto the Robot
1
Build the code
./gradlew build
Compiles Java, checks for errors. Fix anything in the Problems tab in VS Code before deploying.
2
Connect to robot
ping 10.30.91.2
WiFi: connect to 3091-Robot. USB: plug directly into roboRIO USB-B. Ethernet: static IP 10.30.91.5.
3
Deploy
./gradlew deploy
Uploads compiled code to the roboRIO. Ends with BUILD SUCCESSFUL. Robot automatically restarts code.
4
Simulate (no robot)
./gradlew simulateJava
Runs robot code on your laptop. Useful for testing command logic without real hardware.
NOTE: Gradle is the build tool. It downloads dependencies, compiles Java, and packages the code for the roboRIO. You don't need to install Gradle — gradlew is bundled.

## Slide 21
KEY CONCEPTS RECAP
What You Should Know
Command-Based Architecture
Subsystems own hardware. Commands borrow subsystems. The Scheduler manages it all at 50 Hz.
Subsystem = Hardware Wrapper
Each subsystem is one mechanism. Methods like tankDrive(), run(), stop() are the only way to touch motors.
Commands are Actions
execute() runs every 20ms. isFinished() controls when to stop. end() always cleans up.
Constants.java = Single Source of Truth
Change a value in one place. All subsystems and commands read from there.
Triggers vs. Default Commands
Buttons create Triggers that run commands while held. Default commands run when nothing else is active.
Vision = Distance → Speed
PhotonVision provides target pitch. Trigonometry converts pitch to distance. Linear interpolation maps distance to motor speed.

## Slide 22
What's Next?
Ideas for extending this codebase:
Add PID control to the shooter
Use a PID loop to hold the shooter at a target RPM instead of open-loop speed.
Add an encoder to Drive
Use encoders to drive a precise distance in autonomous mode.
Expand vision targeting
Add horizontal alignment — turn to center on the target before shooting.
Add more autonomous routines
Create a SendableChooser on SmartDashboard to let drivers pick the auto at match start.
Add limit switches
Prevent the collector arm from over-extending by adding a hardware limit switch stop.
Team 3091 · REBUILT · FRC 2026 — docs.wpilib.org · photonvision.org · revrobotics.com/sparkmax